## Slide 1
Automated Irrigation System
STM32 Nucleo F446RE · Embedded Systems Final Project
Capacitive Sensing
HAL Drivers
Interrupt-Driven
4-bit LCD
UART Monitor

## Slide 2
Project Overview
The Problem
Manual irrigation is unreliable and labour-intensive. Overwatering wastes resources; underwatering stresses plants. A smarter, automatic system is needed.
The Solution
Continuously monitor soil moisture via a capacitive sensor and automatically engage a 12V pump when moisture drops below a calibrated threshold — with live feedback on an LCD and serial terminal.

## Slide 3
System Components
STM32 Nucleo F446RE
84 MHz Cortex-M4 MCU
Capacitive Soil Sensor
Analog out → PA0 (ADC1)
Relay Module
5V coil, controls 12V pump
LCD1602 (4-bit)
PB4–PB9, real-time display
Manual Override Button
PA4, EXTI4, active-LOW
UART Serial Monitor
115200 baud → PuTTY

## Slide 4
Wiring & Pin Mapping
Pin
Signal
Connected To
Mode
PA0
ADC1_IN0
Sensor AOUT
Analog Input
PA1
Relay IN
Relay module IN
GPIO Output
PA4
Button
Breadboard BTN
EXTI4 pull-up
PB4–PB7
LCD D4–D7
LCD data pins
GPIO Output
PB8
LCD RS
LCD RS pin
GPIO Output
PB9
LCD EN
LCD EN pin
GPIO Output
PA2/PA3
UART2 TX/RX
ST-Link → PC
115200 baud
Power Rails
▸ Sensor VCC → Nucleo 3.3V
▸ Relay coil → External 5V PSU
▸ Pump → External 12V PSU
▸ All GNDs tied to common rail
Shared common ground between all power supplies is critical for signal integrity.

## Slide 5
Firmware Architecture
Interrupt-driven event queue — ISR sets flags, main loop processes them in order
TIM2 ISR
(every 200ms)
Sets doAdcRead flag
ADC Sample
PA0
12-bit, 480-cycle sample
Relay Eval
App_EvaluateRelay()
Threshold check + counter
LCD Update
PB4–PB9
Moisture % + pump state
UART Print
115200 baud
ADC, moisture, threshold
Manual Override (EXTI4 / B1)
External button on PA4 fires a falling-edge interrupt. A 300ms software debounce prevents bounce triggering. Sets manualOverride flag → pump held ON for 10 seconds.
Minimum-ON Counter
Once the pump engages, gPumpOnCounter = PUMP_ON_TICKS (2 ticks = 1 second). Counter decrements each evaluation cycle. Relay stays ON until counter reaches 0, then soil is re-evaluated. Prevents rapid relay cycling.

## Slide 6
Sensor Calibration
2775
Dry ADC
(open air)
1500
Wet ADC
(submerged)
2138
Threshold
(50% moisture)
ADC Range (0 = wet → 4095 = dry)
Threshold
2138
WET ←
→ DRY
Formula: Threshold = DRY − (DRY − WET) × 0.50 = 2775 − 637 = 2138

## Slide 7
Challenges & Debugging
Inverted relay logic
Issue
Trigger-select switch was set to wrong level. Matched RELAY_ON() macro polarity to module behavior.
Relay power instability
Issue
Nucleo's USB 5V rail couldn't sustain coil current. Moved relay to a dedicated external 5V supply with shared GND.
Double-decrement race condition
Issue
Counter was decremented in two places. Consolidated all relay counter logic exclusively inside App_EvaluateRelay().
Spurious EXTI triggers (button bounce)
Issue
Added 300ms software debounce in HAL_GPIO_EXTI_Callback() to block noise-induced override resets.

## Slide 8
Results
Sensor Calibration
Dry=2775, Wet=1500 confirmed via PuTTY. Moisture % tracks linearly and updates every 200ms.
LCD Display
Line 1: 'Moisture: XX %' | Line 2: 'Pump: ON/OFF'. Splash screen on boot, stable 4-bit operation.
Relay & Pump Control
Relay engages reliably at threshold. Minimum-ON counter prevents cycling. LED mirrors pump state.
Manual Override
PA4 and onboard B1 both trigger 10s override. Debounce prevents false triggers. Confirmed in PuTTY.
UART Monitoring
Continuous output: ADC value, moisture %, threshold, pump state — used for live calibration.

## Slide 9
Conclusions & Future Work
Key Takeaways
▸ Inductive loads need isolated power — never share relay coil supply with MCU rails
▸ Relay polarity must be verified empirically, not assumed from silkscreen
▸ Single source of truth for stateful hardware prevents race conditions
▸ Software debounce is essential for EXTI inputs in breadboard environments
▸ Event-queue firmware is modular, readable, and easy to extend
Future Improvements
▸ Store calibration values in flash — no reflash needed to adjust
▸ Add hysteresis band to prevent relay chatter near threshold
▸ RTC integration for scheduled irrigation time windows
▸ OLED upgrade for richer multi-sensor display
▸ Multiple moisture zone support with independent pump channels

## Slide 10
Live Demo
Automated Irrigation System · STM32 Nucleo F446RE
▸ Dry sensor → pump engages
▸ Wet sensor → pump disengages
▸ Button → manual override (10s)
▸ PuTTY → live ADC readout